## Slide 1
Better WASH for quality care in HEALTHCARE FACILITIES
WASH FIT
Methodology
Insert date & location

## Slide 2
Better WASH for quality care in HEALTHCARE FACILITIES
WASH FIT
Methodology
Insert date & location
Notes: Two different covers are available – depending on where the presentation is being used.

## Slide 3: Learning objectives
By the end of this session, you should:
Be aware of how WASH can improve quality of care in health care facilities
Understand the scope of WASH FIT, where it can be used and how
Know how to adapt and use WASH FIT in a range of different settings
Feel confident explaining the WASH FIT methodology to colleagues

## Slide 4
PART 1
Using the WASH Assessment Tool
Understanding WASH FIT- its benefits and process
PART 2
Improving WASH Facilities
Developing an improvement plan
Monitoring progress
Who uses WASH FIT?
How to use WASH Assessment tool?
Analyzing the results of the WASH Assessment

## Slide 5: Word game: “Just a minute”
Turn to the person next to you.
Pick one person to speak, the other person will time.
Explain to your partner, for one minute:
Why is having adequate WASH services in health care facilities important?
You may NOT:
Hesitate (um…. er…. hmmm….)
Deviate (go off topic)
Repeat yourself
3 mins
Note: this works best for face to face audiences. A different “ice-breaker” may be required for virtual audiences
Notes: This works best for face to face audiences. A different “ice-breaker
This icebreaker can be used here or at a different time in the workshop depending on how the workshop is structured. This is based on a game featured on a radio show in the UK and is designed to be a bit of fun!
You could also suggest different questions here. It could be something not related to WASH, e.g. “why should people visit XX country” or anything to get people talking.

## Slide 6: BREAKOUT ROOMS or GROUP DISCUSSION What are the main problem related to WASH in HCF in your country/region/district/facility? In your opinion, what would encourage people to seek care at a facility?
5 mins
Notes: Write ideas on flip chart.
At the end of the session, please record these notes and share with washinhcf@who.int. The information collected will be helpful to understand what are the most common challenges found across countries/regions. You should also use the answers generated during the discussion to help identify what improvements are most needed and which technical modules to focus on.
This may have been covered in the introductory module so could be omitted.

## Slide 7: What is WASH FIT?
What it is
A methodology to improve quality of care through safer, environmentally sustainable & climate-smart WASH infrastructure and services
For facilities to identify areas for improvement and take action
A stepwise approach for making long term changes
For a range of settings, but predominately primary and secondary facilities
What it is not
A tool for national level monitoring of WASH in health care facilities
A one-size fits all approach
An exercise that can be completed in a day
Notes: WASH FIT was initially designed for small (e.g. primary), resource constrained facilities but has also been used in bigger facilities (e.g. district hospitals and in some instances, larger national hospitals). The tool works best in smaller facilities but can be adapted for bigger facilities. The methodology should remain the same but the assessment form will need to be adapted (i.e. adding additional indicators to cover more complex settings such as requirements for major surgical and invasive procedures).

## Slide 8: Improved quality of care through WASH FIT
Notes: WASH FIT helps facilities to understand the general situation in a facility, assess and prioritize where improvements are most needed with the ultimate goal of improving quality of care.

## Slide 9
What does WASH FIT cover?
Add suggestions in the chat box.
Time 1-2 minutes.

## Slide 10
Water supply, storage, water quality testing,
What does WASH FIT cover?
ULTIMATE AIM: Improve quality of care
Waste, from generation to final disposal
Energy (lighting, pumping, heating)
Management, protocols, problem reporting
Hand hygiene
Environmental cleaning & disinfection
Health workforce, training & occupational health
Notes: Looking at the picture, what are the main areas that you would be interested in measuring and improving?
For each of the areas shown here, there are indicators in the assessment form to guide a facility to assess, prioritize, improve & re-asses.
If there are other areas of a facility that are of interest, these can also be added to the assessment form.

## Slide 11
Sanitation, from toilets to treatment
Ventilation, laundry, kitchen, vector control
Climate resilience, reliable energy access and environmental sustainability
Notes: Outside of the facility – WASH FIT includes all elements within a facility compound.

## Slide 12
1. Prepare and train the team and undertake continuous professional development
2. Conduct facility assessment
3. Identify and prioritize areas for improvement
5. Reflect, adapt, improve, learn
4. Develop improvement plan and TAKE ACTION
Methodology
Before starting: Leadership, political commitment & community engagement through
EIGHT PRACTICAL STEPS
Notes: The next slides go through each of the five steps. We begin with step 2 going clockwise, through to Step 1 at the end. This is because it is helpful to know what the process involves before we discuss who should be responsible for WASH FIT activities.
Note, it is a cyclical process, starting at 1, going through to 5, where you should then begin again at 1. It is not an exercise that can be completed as a one-off activity but should become routine within a facility’s work.
The process is based on the WHO Water Safety Planning (WSP) methodology, although the number of steps has been simplified to only 5.
For more information on WSPs, visit: https://www.who.int/water_sanitation_health/water-quality/safety-planning/en/
Before starting, it is important to ensure the enabling environment is in place – refer to the introductory module which describes how WASH FIT fits into the 8 practical steps,

## Slide 13: Steps for Task 1
engage senior management support
Identify team members based on required expertise
Appoint a Team Leader
Define roles and responsibilities
Define the time frame of the implementation of WASH FIT
Establish a dedicated WASH FIT team that can successfully drive the WASH FIT process*
  *Do not create a new team if there is an existing IPC, quality improvement, health care waste management or multi-sectoral planning committees.

## Slide 14: Who should be on the WASH FIT team?
© Shumon Ahmed/CDD
People with knowledge in WASH and IPC to contribute to better problem-solving and a range of potential solutions for WASH improvement issues in the facility.
Cleaning and maintenance workers because they are more familiar with the usage of WASH facilities
Female staff and patient representative to ensure women’s needs are met and included in the plan  Gender representation
Representative from local Disabled People’s Organisation (DPO) to ensure infrastructure and services are accessible and usable  Disability friendly & inclusive services
External stakeholders and partners for additional support especially in small facilities.
Notes: Refer to slide XX for a group exercise on establishing a team, to be included if time allows.

## Slide 15: Example WASH FIT teams, adapted from guidance for Philippines
Primary Health Care Facility | Hospital
Head of the facility ( Team Leader) Nurse Member of community health or water committee Maintenance and/or cleaning personnel WASH officer/Sanitary Inspector Local disability organization representative | Chief /Medical Director/ Facility Administrator Members of the IPC Committee Pollution Control Officer (PCO) or Waste Management Officer (WMO) Nurse per department or division Technician responsible for equipment maintenance Member of community health/water committee City/Municipal Health Officer Maintenance/cleaning staff representative
External members (other stakeholders) | 
Local government unit (LGU) / LDWQMC / WASH Council or Task Force representative Representative from Non-Governmental Organizations (NGOs) or Professional Organizations related to public health interest Local WASH experts / Academia / Representative from Medical or Allied Medical Schools Representative from water districts / water suppliers / water regulators | 

## Slide 16: Roles and Responsibilities of WASH FIT Team
Lead
Establish the vision and commitment of the team and process Ensure that specific tasks and tools are being completed correctly and in a timely manner. Ensure that meetings are held on a regular basis Recruit personnel with skills or expertise as needed Explore opportunities for external support as needed
Members
Conduct regular assessments, identify areas for improvement Attend regular team meetings to discuss reports, findings, potential and emerging problems. Identify and prioritize actions and projects necessary to improve WASH in the facility. Document the process, results, outcomes and impact of WASH FIT

## Slide 17
ADAPT
Review and finalize indicators
1
ASSESS
Conduct comprehensive assessment
2
SCORE
Review assessment and calculate score
3
SCHEDULE next assessment
5
REVIEW & RECORD findings & share with relevant authorities
4
Step 2: Conduct facility assessment

## Slide 18: ADAPT Adapting the assessment tool
First, adapt to match national standards
Add further questions for other areas of interest and higher service levels, e.g. climate and greening, IPC core components
Simplify for small facilities (remove non-applicable indicators, e.g. for in-patients)
Focus on a specific department or ward (ward-level analysis)
Focus on a specific WASH domain, e.g. water or health care waste
Notes: This is often done at the national level before the first training takes place. This slide can be skipped if so, or included if participants are interested to know the process.

## Slide 19: Facility assessment options
Global guide (2018): PDF format
https://www.who.int/water_sanitation_health/publications/water-and-sanitation-for-health-facility-improvement-tool/en/
Updated version (2020): Excel
Simplified version (2020): Kobo Toolbox
https://www.washinhcf.org/resource/wash-fit-simplified-covid-19/
 All can be adapted to local context
Notes: 2018 Guide: PDF format
2020 updates: Excel
2020 simplified version in Kobo Toolbox.

## Slide 20: Facility assessment
Indicator: | Meets: | Partially meets: | Does not meet:
Waste correctly segregated at all waste generation points | Yes (2) | Some sorting but not all correctly or not practiced throughout the facility (1) | Waste not correctly sorted at any waste generation points (0)
Global indicators based on WHO Essential Environmental
Health Standards (2008)
Each indicator scored according to three levels:
  Meets minimum standards – (maintenance needed to sustain score) (scores 2)
  Meets some but not all standards (Needs minor improvement) - (scores 1)
  Does not meet standards (Needs major improvement) - (scores 0)
Example:
Notes: The indicators are based on the WHO global standards “the green book”. The WHO/UNICEF Joint Monitoring Programme indicators (snapshot top right) are also included in the assessment tool. However, the format is different to those used in a national survey and therefore should not be used in their current form for national level monitoring. The assessment tool is designed for facilities to assess their current status and work out where improvements are needed.
For each indicator, there are three criteria listed for the facility to score against. These are based on global standards or other technical guidance but may be adapted according to a given context.
You may also use a different scoring system (e.g. 1,2,3 or stars). Decide as a team what you wish to use.
For many indicators, there are explanatory notes which provide links to further technical resources or information which may be needed to make the assessment.
WHO Global standards: https://www.who.int/water_sanitation_health/publications/ehs_hc/en/
Core questions: https://www.who.int/water_sanitation_health/publications/monitoring-wash-in-health-care-facilities-aug-2018.pdf

## Slide 21: Facility Assessment (New version under development)
“Domains”
Water
Sanitation
Hand hygiene & cleaning
Health care waste
Energy & environment
Management & workforce
Climate integrated throughout
Notes: This slide shows what the assessment tool looks like to give you an idea. This is being updated and a revised version will be ready in April 2020. Please sign up to the newsletter at www.washinhcf.org to receive updates.
The assessment form is split into 6 sections or “domains”. These are made up of essential and advanced indicators. All facilities, should consider including essential indicators while advanced ones are more applicable for higher levels of service (tertiary hospitals or higher income settings).

## Slide 22: WASH FIT assessment tool
General information
Water – 9 indicators
Sanitation – 9 indicators
Health Care Waste Management – 10 indicators
Hand Hygiene – 6 indicators
Environmental Cleaning - 8 indicators
Energy & Environment – XX indicators
Management – 8 indicators
Climate integrated throughout
Edit list according to final list of WASH FIT indicators in national/facility context
Notes: Update number of indicators to match the local context

## Slide 23: How to complete the assessment
Conduct a physical inspection of all the areas of the health facility.
Rate each indicator – does the facility:
  meet standards? (score = 2)
  partially meet standards? (score = 1)
  not meet standards? (score = 0)
Specify further details in “Comments” section (250 characters limit)

## Slide 24: SCORE Calculating WASH FIT assessment score
Used to:
track progress over time in a facility
make comparisons between facilities
How to calculate:
Numerator: Total number of points across all indicators
Denominator: Maximum possible score, calculated by number of indicators assessed x 2.
  Denominator may be calculated across the domain, ward or the whole facility.
Calculate every six months (or more often if preferred)
Suggested cut off points:
< 67% Red (major efforts and resources needed for improvements, across all domains)
67-75% Yellow (additional efforts are needed and ongoing maintenance)
> 75% Green (facility is doing well but a small number of indicators could still be improved)
Notes: The score will help to get an overall picture of the facility. It is a crude score because all indicators are weighted the same (i.e. whether the facility has an improved water supply contributes the same as whether there is lighting in the latrines).
The score can be used to measure progress over time, however it is important to remember that the score may go up overall, while some important indicators go down during the same period.
The cut off points are just a suggestion, you may wish to use different criteria. This should be agreed on a national basis or at the facility level by the WASH FIT team. An example from Liberia is presented on the next slide

## Slide 25: Weighting
Final score is a percentage (%) meaning “essential indicators” make up a bigger proportion of the score.
Indicator | Weight | 
Essential | 2 (worth twice as much) | 
Advanced | 1 (i.e. no weighting) | 

## Slide 26: Calculate the missing information in the table below
Example scoring (no weighting) | Number of indicators fully meeting minimum standards (2) | Number of indicators partially meeting minimum standards and can still be improved (1) | Number of indicators that do not meet standards (0) | Total across all indicators (Numerator) | Number of indicators assessed | Maximum score (Indicators x 2) (Denominator) | Domain score (%)
Water | 4 | 2 | 3 | 10 | 9 | 18 | 56
Sanitation | 5 | 1 | 3 | 11 | 9 | 18 | 61
Health care waste | 8 | 2 | 0 | 18 | 10 | 20 | 90
Hand hygiene | 5 | 0 | 1 | 10 | 6 | 12 | 
Environmental cleaning | 3 | 2 | 3 | 8 | 8 | 16 | 50
Management | 2 | 4 | 2 | 8 | 8 | 16 | 50
OVERALL WASH FIT SCORE |  |  |  | 65 | 50 | 100 | 
Notes: This provides an example from a hypothetical facility. We will revisit the same facility throughout the technical modules.
In a small, rural health care facility where there are only a couple of staff, no deliveries, many of the indicators are not applicable and therefore only 30 indicators were assessed.
If you have used WASH FIT already, you may wish to change this slide to a real example of a facility.

## Slide 27
Example scoring (no weighting) | Number of indicators fully meeting minimum standards (2) | Number of indicators partially meeting minimum standards and can still be improved (1) | Number of indicators that do not meet standards (0) | Total across all indicators (Numerator) | Number of indicators assessed | Maximum score (Indicators x 2) (Denominator) | Domain score (%)
Water | 4 | 2 | 3 | 10 | 9 | 18 | 56
Sanitation | 5 | 1 | 3 | 11 | 9 | 18 | 61
Health care waste | 8 | 2 | 0 | 18 | 10 | 20 | 90
Hand hygiene | 5 | 0 | 1 | 10 | 6 | 12 | 83
Environmental cleaning | 3 | 2 | 3 | 8 | 8 | 16 | 50
Management | 2 | 4 | 2 | 8 | 8 | 16 | 50
OVERALL WASH FIT SCORE |  |  |  | 65 | 50 | 100 | 65%
Notes: This provides an example from a hypothetical facility. We will revisit the same facility throughout the technical modules.
In a small, rural health care facility where there are only a couple of staff, no deliveries, many of the indicators are not applicable and therefore only 30 indicators were assessed.
If you have used WASH FIT already, you may wish to change this slide to a real example of a facility.

## Slide 28
Example scoring (no weighting) | Number of indicators fully meeting minimum standards (2) | Number of indicators partially meeting minimum standards and can still be improved (1) | Number of indicators that do not meet standards (0) | Total across all indicators (Numerator) | Number of indicators assessed | Maximum score (Indicators x 2) (Denominator) | Domain score (%)
Water – Essential (weighted x 2) | 2 | 1 | 2 | 2 x 2 x 2 1 x 1 x 2 2 x 0 x 2 = 10 | 5 | 5 x 2 x 2 = 20 | 50%
Water – Advanced (no weighting) | 4 | 2 | 4 | 2 x 2 1 x 1 2 x 0 = 5 | 10 | 5 x 2 = 10 | 50%
Sanitation – Essential | 5 | 0 | 0 | 11 | 5 | 20 | 
Sanitation – Advanced | 0 | 2 | 2 |  | 4 | 8 | 
OVERALL WASH FIT SCORE |  |  |  | 65 | 50 | 100 | 65%
Notes: This provides an example from a hypothetical facility. We will revisit the same facility throughout the technical modules.
In a small, rural health care facility where there are only a couple of staff, no deliveries, many of the indicators are not applicable and therefore only 30 indicators were assessed.
If you have used WASH FIT already, you may wish to change this slide to a real example of a facility.

## Slide 29: Liberia: facility score determines level of attention required
Quarterly assessment
VERY POOR (0 - 45%)
 Needs immediate attention
POOR (46 - 64%)
 Needs urgent attention
MEDIUM (65 – 79%)
 Needs attention
GOOD (80 - 100%)
 Still needs continuous supportive supervision
Notes: The snapshot shown here are the results from all facilities in a district. Scores are given for each domain for a 6 month period. The facilities were reassesed after 6 months.

## Slide 30: Philippines: Star rating awarded to facilities
RATING | REMARKS | ACTION REQUIRED
100% THREE STAR | MAINTAIN YOUR RATING. | Maintain your rating. Do the next assessment after one year.
75%-99% TWO STAR | (NO score of zero in any of the indicators) CONTINUE MAKING IMPROVEMENTS to fully meet the minimum national standards. | Address indicators that scored ONE. Do the next assessment after six months.
50%-74% ONE STAR | (NO score of zero in any of the indicators) ADDITIONAL IMPROVEMENTS NEEDED to fully meet the minimum national standards. | Address indicators that scored ONE. Do the next assessment after six months.
50%-99% CONDITIONAL PASS | (With a score of zero in any of the indicators) ADDITIONAL IMPROVEMENTS NEEDED to confirm your rating. | Address indicators that scored ONE OR ZERO. Do the next assessment after three months.
Below 50% NO STAR | (HAS A score of zero in any of the indicators) CRITICAL CHANGES NEEDED IMMEDIATELY. Use the result of the assessment to address indicators that are not meeting minimum national standards to come up with an improvement plan and to guide you in implementing these changes. | Address indicators that scored ONE or ZERO. Do the next assessment after three months.

## Slide 31: Data visualization by domain in Kenya (1)
% of indicators scoring 0, 1 or 2 across four domains
Comparison of 16 district hospitals
Highest scoring domain = water
Helpful for government/policy makers to compare facility performance
Drives interest and consistent performance for facility staff
Notes: It is useful to show how facilities are doing. These graphs compare 16 district hospitals in Kenya. The same graph format could be used to show the same facility over time, or to compare different wards within a facility.
The best performing domain, across all hospitals, was water (bottom row, with the most green).

## Slide 32
“Heat map” by individual indicator (scored 0, 1 or 2)
Shows particular areas of weakness
Helps identify where improvements are needed
Data visualization by indicator in Kenya (2)
Notes: An alternative is to look at the indicator level.

## Slide 33
WASH FIT INDICATOR Reference Number | INDICATOR | RATING
1.2 | Water services available at all times and of sufficient quantity | 2- Water services available every day and of sufficient quantity 1- Water services available more than 5 days per week or every day but not sufficient quantity 0- Water services available fewer than 5 days per week
To calculate the facility’s water requirements, add up the following applicable national standards:
Outpatients: 5 L/consultation
Inpatients: 40–60 L/patient/day
Operating theatre or maternity unit: 100 L/intervention
Dry supplementary feeding center: 0.5–5 L/ consultation depending on waiting time
Wet supplementary feeding center: 15 L/ consultation
Cholera treatment center:60 L/patient/day
Severe acute respiratory diseases/isolation center: 100 liters/patient/day
Viral hemorrhagic fever isolation center: 300–400 liters/patient/day
Example training slide from the Philippines
Notes: The following slide is an example from WASH FIT training in the Philippines. Every indicator was presented, with the criteria for the notes explained in detail. This may be needed for facility level trainings but may not be needed at the national level. Adapt the slides according to audience and time available.

## Slide 34
WASH FIT INDICATOR Reference Number | INDICATOR | RATING
1.3 | Reliable drinking water station available | 2- A reliable drinking water station is present at all times and locations and accessible to all 1- A reliable drinking water station is present sometimes, or only in some places or not available for all users 0- A reliable drinking water station is not available
1.4 | Drinking water safe storage | 2- Yes, all available drinking water is safely stored with cover and tap 1- Some of the available drinking water points are safely stored 0- Drinking water points are not safely stored or no drinking water available
This refers to water dispenser or water containers with cover and tap

## Slide 35: Facility vs. ward level indicators Adapting WASH FIT for bigger facilities
Facility-level data may not be a true reflection of the situation on the ground for larger facilities with several in-patient units
Ward-level indicators can identify variations between hospital departments/ wards
Useful for hospital management to identify poor performing wards and direct resources where most needed
Helps priority setting for quality improvement activities by hospital managers & committees
Notes: Some indicators are difficult to measure at the facility level because they do not capture enough detail nor show variation across wards. For example. Looking at available and usable toilets in a district hospital. These may vary differently in different departments (e.g. toilets may not function in the delivery area but be in good condition in the emergency department). You may wish to assess certain indicators at multiple points across a facility. These indicators are labelled in the assessment tool with “ward”.

## Slide 36: Breakout rooms
Look at the photos on the next slide.
For each picture, discuss in groups:
What information would you need to check to see if the standards are met?
What are the relevant indicators?
Are there things you cannot see in the picture that you would need to ask staff about?
You may refer to the WASH FIT assessment for help.
10 mins
Notes: Each group should be given one picture to focus on and report back to the main group. They may then discuss other pictures if there is time.

## Slide 37: For each picture, what aspects do you need to assess / ask about?
1
2
3
4
Notes: This slide is designed to teach people to be as thorough as possible when doing an assessment. Ask participants to consider what information they need to find in each picture and how they should do it – observation, questions (if so, what type of questions), collect data? You may wish to change the photos in the slide to your own context or use the following slide instead.
Lift up the lids and look inside. Is waste correctly segregated? Are bins labelled? Are there posters with information on the wall? Who is responsible for emptying the bins?
Ask the staff if the water is functioning, does it always function? Is water quality tested? Is there a protocol to take action if the water quality is poor?
look inside the hand washing station, is there water? If so, is it filled every day? If not, why not? What other improvements are needed here?
Open the doors of the latrines and look inside. Don’t just trust what you see on the outside. Consider hand hygiene availability? How is fecal waste managed? Is there onsite treatment?
Be thorough – even if you know the facility well, there may be things that are not as they appear and more probing and questions are needed!

## Slide 38: For each picture, what aspects do you need to assess / ask about?
1
2
3
4
Notes: This is a second option of the previous slide for a higher income setting.

## Slide 39: What possible challenges might the WASH FIT team face when conducting the assessment?
Possible challenges:
Availability and accuracy of relevant information
Limited willingness of senior management to engage
Lack of understanding on the importance of water, sanitation hand hygiene and hygienic practices to prevent and control infections.
Time required by staff to undertake assessment
Breakout rooms / small discussions
Spend a few minutes discussing in small groups
3 mins

## Slide 40
You have completed the assessment of the facility.
As a team, look at the results of the assessment & consider:
What are the major problems identified?
What risks do these problems pose?
What short- and long-term actions can be taken to improve the situation?
What positive things did you find that should be celebrated?
Step 3: Identify areas for improvement
Notes: Remember to look for positives and not only to focus on the negatives in a facility.
Risks: these could be to patients, staff, or the community. They may be linked to infection risk (e.g. public health), to staff morale, to patient satisfaction or affect the community (e.g. from preventing people from accessing services).

## Slide 41: Breakout rooms:
Look at the maternity room pictured here:
What problems can you see in these pictures?
What are the risks?
What issues related to gender, social inclusion & disability do you see?
What are some improvements that could be made?
5 mins
Notes: The aim of this exercise is to start thinking about the range of risks and problems you might face. Think about all different types of risk: public health/infection, staff safety and morale, patient satisfaction and ability to provide quality of care.
Participants should take 5 minutes to discuss in pairs or small groups. After 5 minutes, come together and ask participants to share ideas. Write these on the flip chart.
You may wish to change the pictures to suit your local context.

## Slide 42: Group exercise: prioritization
Your resources are limited and you cannot make all the improvements that are needed.
What criteria would you use to prioritise?
?
At your facility, you have identified the following problems:
There are frequent water shortages (increasingly common due to climate change)
Drinking water is not treated
Toilets are not marked for male and female
Lightbulbs are broken in the delivery room and electricity is unreliable.
Waste not sorted correctly at point of generation
Cleaning staff are not sufficiently trained; no record of cleaning visible.
Notes: The criteria used to prioritize will vary according to the facility. Some may want to focus on quick wins (low hanging fruits), i.e. things that can be done relatively quickly or easily and with limited resources. These things may not have the biggest impact to health/quality of care but are still useful.
By starting with the quick wins (e.g. gender segregation of toilets and broken lightbulbs), it may empower staff to go on to tackle bigger challenges (e.g. water shortages).
There is no right or wrong answer here.

## Slide 43: Polling for possible criteria

## Slide 44
Risk prioritisation in Indonesia
Staff wrote a list of all WASH improvements needed on strips of paper
Staff ranked improvements as a team
Decided own criteria for ranking
Notes: This example is from a catholic hospital in West Timor. The team conducted an assessment, and wrote all the problems they identified (i.e. anywhere that an indicator scored 0 or 1), onto a piece of paper.
As a team, they decided which were the most important things that needed to be addressed.
Please include alternative suggestions from your work if you have them. Again, there is no right or wrong way to do this.

## Slide 45
Indonesia: before and after
Waste outside nutrition clinic identified as a major problem
Cleaning campaign for 1 month
Bins installed for general waste in grounds
Clean surroundings, risk of infection and injury decreased
After
Before

## Slide 46: Step 4: Develop an improvement plan and take action
What improvements are needed? (the long list)
Which improvements should be prioritised in the next 6 months? (the short list)
When and who will complete these actions?
What resources are needed (e.g. technical, human, financial)
It is recommended not to plan any activities longer than 6 months as these are likely to be forgotten. Focus on 1 month, 3 months, 6 months.
Review again in 6 months (Step 5) and reassess what needs doing.

## Slide 47: Step 4: Process
List the specific improvements NEEDED
Identify person/s or group/s responsible for implementing the actions
Determine the resources required to accomplish the plan
Estimated budget and identify source of funds
Set target date of completing the action
ACT and record the date of completion

## Slide 48: Sample improvement plan
INDICATOR | ACTION NEEDED | PERSON RESPONSIBLE | RESOURCES NEEDED | BUDGET | SOURCE OF BUDGET | TARGET DATE | COMPLETION DATE
W1/ W2/ W3 | Install piped water supply from a local water supplier | Head of Maintenance Div. | Application fee Pipe materials (GI or PE) | Application fee @ USD 95 Pipe materials (GI/PE) lump sum @ USD 400 | CAPEX | 3rd quarter of 2021 | To be filled in once activity completed
HM1 | Implement regular training of staff on HCW management and infection prevention and control. | HRD/ COH/ WASH FIT Team | Training materials / Trainor’s fee/ venue | USD 25/ staff @ 50 participants USD 1250 | CAPEX for annual training budget | 2nd quarter of 2021 | To be filled in once activity completed
HM2 | Re-design the temporary storage to allow separation of HCW by categories | Head, Maintenance Div. | Marine plywood / others/ carpentry materials | Marine plywood @USD 35 /board x 8pcs USD 300 Other support woods USD 82 | Special fund request from General Services Div. | 2nd week of September 2020 | To be filled in once activity completed

## Slide 49
Building new infrastructure or repairing old infrastructure (fixing taps) considering key climate variability and changing hazards (e.g. exposure to flooding, cyclones, increase of water temperature or sea-level raise);
Clearing away broken equipment
Reviewing protocols and SOPs
Staff training in new techniques or procedures as well as impacts posed by climate variability and change
Improving management methods
Simple, low cost improvements can still have a big impact
Imagination and creativity may be needed
Incremental improvements

## Slide 50
Improvements in Chad: extremely low-resource setting
Planting plants by HCF entrance
Clear signs demonstrating gender separation of latrines
Hand washing poster drawn by
head of HCF
Photos: Chad 2016, © WHO
Notes: These are examples from a rural primary health care facility with limited resources. They had limited capacity for the “big ticket items” so focused on small manageable things that they could do without external help.

## Slide 51: Improvements in Tajikistan: lower-middle income setting
Water tanks with lid and tap accessible for patients
Sanitation facility adapted for patients with physical impairment
Hand washing posters
Photos: Tajikistan 2019, © WHO

## Slide 52: Improvements in Kenya: assigning responsibility
Different indicators are the responsibility of different groups
  Some above the hospital management* (i.e. county/district level)
  Some delegated to specific persons / groups within the hospital
Need to assign responsibility for specific indicators to people for easy follow up
* includes medical director, Nursing officer in charge, chief administrative officer, hospital management board
Level of responsibility | % of indicators | Example indicators
County level | 14% | Available WASH budget, national water quality standards, availability of piped water supply
Hospital Management with help from country government | 48% | Adequate cleaners & staff, appropriate water treatment & storage, available and usable toilets
Hospital management with help from IPC committee | 38% | Waste segregation, hand hygiene promotion activities
Notes: In this example from Kenya, the WASH FIT team realized that specific people had responsibility for different areas within a facility and it was helpful to divide these up at the start. The following slide shows how every indicator was assigned.

## Slide 53
Notes: Kenya example: This slide shows how the hospital decided to assign responsibility for certain indicators to different levels. Ask participants if there are any that they disagree with? How would they do it differently? Would it be helpful to do this in their own setting?
Are there different stakeholders that should be given responsibility?

## Slide 54: Step 5: Reflect, adapt, improve and learn
Every 6 months, conduct assessment and re-calculate the WASH FIT score
How has the facility score changed since the last assessment?
Which domains have improved? (Remember the overall score may improve, but important indicators can still go down)
Which domains (or indicators) are scoring less well and why?
Do you need to ask for external help? Is there particular expertise missing?
Is there capacity to address new areas of the facility?
Notes: Monitoring confirms progress towards reaching the targets of each domain
Build monitoring into staff job descriptions
Ensure there is a monitoring lead and that the health facility manager is engaged
Primary aim is to improve processes internally but sharing of results with district and other stakeholders is important for long-term change
Monitoring is not about blaming, but about recognizing improvements and addressing ongoing problems

## Slide 55
Other considerations for success

## Slide 56: What challenges might the WASH FIT team face?
Technical capacity of team members
Engaging stakeholders & senior management
High workload – limited time for WASH FIT activities
Maintaining a consistent and effective communication between the WASH FIT team members
Ensuring all voices are heard – gender, race, age, clinical vs. non-clinical
Scheduling regular meetings of the WASH FIT team together and sustaining initiatives
Add suggestions to chat box, or if time, use breakout rooms for a quick discussion
3 mins

## Slide 57: Breakout rooms
Chose either Facility 1 or 2 (or your own facility, if relevant):
Who should be responsible for WASH FIT activities?
What external expertise would you need to bring in?
What management structures or teams are already in place? How could you integrate WASH FIT into these structures?
What challenges might arise?
Rural primary health care centre
1 nurse, 1 health assistant
No deliveries
3 hours drive from the capital,
District hospital situated in a large town, 2 hours from the capital
100 beds, 10 deliveries per week, large town 2 hours from the capital,
1
2
10 mins
Notes: Divide into small groups. Half the participants may look at scenario 1 and half scenario 2
Brainstorm among the group to answer the questions.
The pictures are from 2 facilities in Bhutan. You may like to replace the photos with examples from your setting. If there are specific teams or structures (e.g. quality improvement teams are common) which are common in your setting, consider these.
Highlight: LEADERSHIP IS KEY. A lot can be achieved with limited resources if there is a leader who is active and engaged.
Possible challenges – resistance to change, perception of high work load and something ‘extra’, lack of knowledge and expertise to do it.

## Slide 58: Leadership drives & sustains change Domain: “Management & health workforce”
Ensuring good management & a sufficient workforce will help the facility to meet all technical requirements
One committed individual can make a huge difference, and thereby improve the quality and safety of health services.
Leaders should bring vision and commitment
Create a culture of quality improvement throughout the facility
All staff are listened to and respected
Notes: The “Management & health workforce” domain of WASH FIT is as important as the technical domains (Water/Sanitation/Hand hygiene/Environ. Cleaning/HCWM.
The indicators cover training, staffing, protocols and policies. These help facilities to implement all the technical domains and should not be overlooked.
Ask participants: do they have good examples of leadership to share? What qualities did they have? Why were they successful?
How would you create a culture of quality improvement in a facility?

## Slide 59: Building a culture of quality improvement at a district hospital in Ethiopia
1
3
4
5
6
2
A committed leader
Staff incentivized with awards for good performance
A formally recognized quality management system includes WASH
Regular audits of WASH & IPC
Wards ranked according to WASH FIT score & shown at facility entrance
Hand hygiene activities
Leadership drives & sustains change

## Slide 60: Engaging the community
Include at least 1 community representative on the WASH FIT team
Involve vulnerable groups – minorities, local disabled persons group, women – and faith-leaders
Particularly important to involve the community if the facility & community share a water source
In a rural PHC in Ghana, a community committee:
Planned a cleaning campaign to improve health care waste management
Engaged a local engineer/technician who helped fixed blocked taps, mend windows and build a fence around the facility to prevent animals entering
Appeared on the local radio station asking community members to report problems they had encountered at the HCF
Photo: Members of the community committee inspect the waste pit with the IPC focal point to plan improvements

## Slide 61: Small group role play (option 1)
Convincing senior management why WASH is important
Person 1: You have been to a WASH FIT training and return to your facility. You have to convince the facility manager of the important of WASH in HCF and why they should invest in WASH.
Person 2: You are the facility manager and you think you have already got too much work to do. You are not interested in putting time and money into improving WASH.
10 mins
Notes: This can be done as part of this module, or in the training skills module. It may also be done as a revision exercise, in breakout groups or in plenary.
Once the group is back together, ask someone to share their experience.
Person 1 - how did you feel?
What arguments did you both use?
Did you use persuasion? Evidence? Jokes?
What challenges do you think staff might find when they talk to management?

## Slide 62: Small group role play (option 2)
Person 1: You are the manager of the HCF and you have to explain the methodology of WASH FIT and the benefits of using it to your staff
Person 2 & 3: You have never heard of WASH FIT before and you do not understand the approach. You ask person 1 many questions about WASH FIT to try and understand more.
10 mins
Notes: This can be done as part of this module, or in the training skills module. It may also be done as a revision exercise, in breakout groups or in plenary.

## Slide 63
Questions?

## Slide 64: References
WHO/UNICEF 2018. Water and Sanitation for Health Facility Improvement Tool (WASH FIT). http://www.who.int/water_sanitation_health/publications/water-and-sanitation-for-health-facility-improvement-tool/en/ (updated version due late 2020)
WHO, 2008. Essential environmental health standards in health care. www.who.int/water_sanitation_health/publications/ehs_hc/en/.
WHO, 2014. Safe management of wastes from health care activities. Second Edition. World Health Organization, Geneva. www.who.int/water_sanitation_health/publications/safe-management-of-wastes-from-healthcare-activities/en/
WHO, 2017. Safe management of wastes from health care activities: a summary. World Health Organization, Geneva. www.who.int/water_sanitation_health/publications/safe-management-of-waste-summary/en/
WHO, 2019. Overview of treatment technologies for infectious and sharp waste from health care facilities. www.who.int/water_sanitation_health/publications/technologies-for-the-treatment-of-infectious-and-sharp-waste/en/
WHO (2016) Standards for improving quality of maternal and newborn care in health facilities http://www.who.int/maternal_child_adolescent/documents/improving-maternal-newborn-care-quality/en/#
WHO (2016) Global guidelines on the prevention of surgical site infection http://www.who.int/gpsc/ssi-guidelines/en/
WHO Clean Care is Safer Care http://www.who.int/gpsc/5may/en/